## Slide 1: Digital Logic Circuits

## Slide 2
Computer Architecture
is concerned with the structure and behavior of the computer from the user’s point of view.
It is the external view of the computer that anyone who is likely to program a computer should understand.
Computer Organization
is concerned with the way that hardware components operate and the way they are connected to form the computer.
It is the internal view of the computer and the roles various internal components play during program execution.
Computer Design
is concerned with the hardware design of the computer.
It is concerned with decisions like which hardware should be used and how they should be connected.

## Slide 3: In this lecture, we will study
Logic gates
Boolean algebra
K-maps and K-map simplification
Combinational circuits (half adder, full adder)

## Slide 4: Logic Gates

## Slide 5: Logic Gates
In order to manipulate binary information, logic circuits called gates are required.
Gates are blocks of hardware that produce an output of either 0 or 1, depending on the given inputs.

## Slide 6
Types of Logic Gates
AND
OR
Inverter (aka NOT)
Buffer
NAND
NOR
Exclusive OR (XOR)
Exclusive NOR (XNOR)

## Slide 7: Logic Gates
Name
Symbol
Algebraic Function
Truth Table
AND
x=A*B or x=AB
A B x
0 0 0
0 1 0
1 0 0
1 1 1
OR
x=A+B
A B x
0 0 0
0 1 1
1 0 1
1 1 1

## Slide 8: Logic Gates
Name
Symbol
Algebraic Function
Truth Table
Inverter (aka NOT)
x
x=A’
A
x
0
1
1
0
Buffer
x
x=A
A
x
0 0
1 1

## Slide 9: Logic Gates
Name
Symbol
Algebraic Function
Truth Table
NAND (Not AND)
x=(AB)’
A B x
0 0 1
0 1 1
1 0 1
1 1 0
NOR (Not OR)
x=(A+B)’
A B x
0 0 1
0 1 0
1 0 0
1
1
0

## Slide 10: Logic Gates
Name
Symbol
Algebraic Function
Truth Table
Exclusive OR (XOR)
x=AB
or
x= A’B+AB’
A B x
Exclusive NOR (XNOR)
x=(AB)’
or x=A’B’+AB
0 0 0
0 1 1
1 0 1
1 1 0
A B x
0 0 1
0 1 0
1 0 0
1
1
0

## Slide 11: Exercise
Draw a logic diagram for the following Boolean expression:
F=AB+A’C

## Slide 12: Exercise
A
C
A
B
AB
AC
F=AB+A’C

## Slide 13: Exercise
F=AB+A’C

## Slide 14: Exercise

## Slide 15: Boolean Algebra

## Slide 16: Boolean algebra is the algebra that deals with binary variables and logic operations.
Binary Variables: A, B, x, y, etc.
Basic Logic Operation: AND, OR, Complement

## Slide 17: A boolean function is expressed using binary variables, logic operation symbols, paratheses, and an equal sign (=).
For instance,
F = x+y’z
is a boolean function, where the function F is equal to 1 if x is 1 or if both y’ and z are equal to 1, and 0 otherwise.

## Slide 18: Other Representations of a Boolean Function
Algebraic Logic Diagram Truth Table Expression
F = x + y’ z
x | y | z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 19: Identities and DeMorgan’s Theorem

## Slide 20: Identities: List of axioms and theorems
Identity | A + 0 = A | A. 1 = A
Complement | A + A’ = 1 | A. A’ = 0
Commutative | A + B = B + A | A. B = B. A
Assosiative | A + (B + C) = (A + B) + C | A. (B. C) = (A. B). C
Distributive | A. (B + C) = A. B + A. C | A + (B. C) = (A + B). (A + C)
Null Element | A + 1 = 1 | A. 0 = 0
Involution | (A’)’ = A | 
Indempotency | A + A = A | A. A = A
Absorption | A + (A. B) = A | A. (A + B) = A
Distributive | A + A’. B = A + B | A’ + A.B = A’ + B
De Morgan’s | (A + B)’ = A’. B’ | (A. B)’ = A’+ B’

## Slide 22
F= ABC+ABC’+A’C F= AB(C+C’)+A’C F= AB(1)+A’C
F= AB+A’C

## Slide 23: DeMorgan’s Theorem is crucial for dealing with NAND and NOR gates.
NOR gate: The function (x+y)’ is equivalent to (x’y’).
NAND gate: The function (xy)’ is equivalent to (x’+y’).
For this reason, NOR and NAND gates haves two distinct graphical symbols.

## Slide 24: Two graphical symbols for NOR gate
Two graphical symbols for NAND gate
Both NOR and NAND gates are called UNIVERSAL GATES

## Slide 25: K-Maps

## Slide 26: Why K-Maps?
Complexity can be reduced by simplifying the Boolean algebraic expression
with the help of Karnaugh Map or K-Map.
Increase in complexity of Boolean algebraic expression
Increase in complexity of logic diagram

## Slide 27: K (Karnaugh)-maps
Maurice Karnaugh introduced it in 1953
K Map is a graphical representation used for simplifying the Boolean expressions.
For a Boolean expression consisting of n-variables, the number of cells required in K Map = 2n cells.
K Map is based on the Grey code(Unit distance code).
K Map is based on three types of Input values(0, 1, don't care)

## Slide 28: Minterms
A B C F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A minterm is a Boolean expression resulting in 1 for the output of a single cell, and 0s for all other cells in a Karnaugh map or a truth table.
In this sample truth table, we have five minterms, namely:
A’B’C, AB’C’, AB’C, ABC’, and ABC
(because for F= A’B’C, F=AB’C’, F=AB’C, F=ABC’, and F=ABC , the
output is 1, and for all other Boolean expressions, the output is 0).

## Slide 29: Representing Truth Tables as Minterms
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
F(A, B, C) = Σ (1, 4, 5, 6, 7)
=
Here, the cells 1, 4, 5, 6, and 7 represent the minterms.

## Slide 30: K-Maps
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
F(A, B, C) = Σ (1, 4, 5, 6, 7)
0 | 0 | 1 | 1 | 3 | 0 | 2 | 0
4 |  | 5 |  | 7 |  | 6 | 
 | 1 |  | 1 |  | 1 |  | 1
B, C
=
A
00
01
11
10
0
1

## Slide 31: K-Maps for 2, 3, and 4 variable functions
0 | 1 | 3 | 2
4 | 5 | 7 | 6
B, C
00
01
11
10
A
0
1
0 | 1
2 | 3
B
0
1
A
0
1
0 | 1 | 3 | 2
4 | 5 | 7 | 6
12 | 13 | 15 | 14
8 | 9 | 11 | 10
C, D
00
01
11
10
A, B
00
01
11
10

## Slide 32: Karnaugh Maps - Rules of Simplification

## Slide 33: Karnaugh Maps - Rules of Simplification

## Slide 34: Karnaugh Maps - Rules of Simplification

## Slide 35: K-Map Simplification
F(A, B, C) = Σ (3, 4, 6, 7)
0 | 0 | 1 | 0 | 3 | 1 | 2 | 0
4 |  | 5 |  | 7 |  | 6 | 
 | 1 |  | 0 |  | 1 |  | 1
B, C
00
01
11
10
A
0
1

## Slide 36: K-Map Simplification
F(A, B, C) = Σ (3, 4, 6, 7)
0 | 0 | 1 | 0
1 | 0 | 1 | 1
B, C
00
01
11
10
A
0
1

## Slide 37: K-Map Simplification
00 | 01 | 11 | 10
0 | 0 | 1 | 0
1 | 0 | 1 | 1
B, C
A
0
1
F= BC+ AC’

## Slide 38: K-Map Simplification
00 | 01 | 11 | 10
0 | 0 | 1 | 0
1 | 0 | 1 | 1
B, C
A
0
1
F= BC+ AC’ + AB
Additional term
Consider Essential prime implicants

## Slide 39: K-Map Simplification
F(A, B, C, D) = Σ (0, 2, 5, 7, 8, 10, 13, 15)
1 | 0 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
C, D
00
01
11
10
A, B
00
01
11
10

## Slide 40: K-Map Simplification
1 | 0 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
F(A, B, C, D) = Σ (0, 2, 5, 7, 8, 10, 13, 15)
C, D
00
01
11
10
A, B
00
01
11
10

## Slide 41: K-Map Simplification
38
A, B
00
01
11
1 0 0 1
0 1 1 0
0 1 1 0
10 1 0 0 1
C, D
00 01 11 10
F= BD+ B’D’
(other solutions are also possible)

## Slide 42: Exercise
F(A, B, C, D) = Σ (1, 3, 4, 5, 6, 9, 11, 12, 13, 14)

## Slide 43: Exercise
0 | 1 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 0 | 1
0 | 1 | 1 | 0
F(A, B, C, D) = Σ (1, 3, 4, 5, 6, 9, 11, 12, 13, 14)
C, D
00
01
11
10
A, B
00
01
11
10

## Slide 44: Exercise
0
1
1
0
1
1
0
1
1
1
0
1
0
1
1
0
F(A, B, C, D) = Σ (1, 3, 4, 5, 6, 9, 11, 12, 13, 14)
C, D
00
01
11
10
A, B
00
01
11
10
41

## Slide 45: Exercise
1
1
0
1
1
0
1
1
1
0
1
0
1
1
0
C, D
00
01
11
10
A, B
00 0
01
11
10
F= BC'+B'D+BCD’

## Slide 46: The maps we have seen so far can also be referred to as the ‘SUM OF PRODUCTS’ form of K-Maps
0 1 1 0
1 1 0 1
1 1 0 1
0 1 1 0
C, D
00 01 11 10
A, B
00
01
11
10
F= BC+B’D+BCD’
(other solutions are also possible)
F(A, B, C, D) = Σ (1, 3, 4, 5, 6, 9, 11, 12, 13, 14)

## Slide 47: Another Representation of K-Maps:
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
F(A, B, C) = Π (0, 2, 3)
=
Product of Sums (POS)

## Slide 48: Maxterms
A B C F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A maxterm is a Boolean expression resulting in 0 for the output of a single cell, and 1s for all other cells in a Karnaugh map or a truth table.
In this sample truth table, we have three maxterms, namely:
A+B+C, A+B'+C, and A+B'+C'
(because for A+B+C, A+B'+C, and A+B'+C', the output is 0, and for all other Boolean expressions, the output is 1).

## Slide 49: Representing Truth Tables as Maxterms
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
F(A, B, C) = Π (0, 2, 3)
=
Here, the cells 0, 2, and 3 represent the maxterms.

## Slide 50
F(A, B, C, D) = Σ (1, 3, 4, 5, 6, 9
11, 12, 13, 14)
0 | 1 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 0 | 1
0 | 1 | 1 | 0
C, D
00
01
11
10
A, B
00
01
11
10
F(A, B, C, D) = Π (0, 2, 7, 8, 10, 15)
SUM OF PRODUCTS
PRODUCT of SUMS

## Slide 51: POS Simplification
1 | 1 | 0 | 1
1 | 1 | 0 | 0
0 | 0 | 0 | 0
1 | 1 | 0 | 1
F(A, B, C, D) = Π (3, 6, 7, 11, 12, 13, 14, 15)
C, D
00
01
11
10
A, B
00
01
11
10

## Slide 52: POS Simplification
1
1
0
1
1
1
0
0
0
0
0
0
F(A, B, C, D) = Π (3, 6, 7, 11, 12, 13, 14, 15)
C, D
00
01
11
10
A, B
00
01
11
1
1
0
1
10
49

## Slide 53: POS Simplification
50
1 1 0 1
1 1 0 0
0 0 0 0
1 1 0 1
C, D
00 01 11 10
A, B
00
01
11
10
F= (C’+D’) (A’+B’) (B’+C’)
(other solutions are also possible)

## Slide 54: 5-Variable K-Maps
0 | 1 | 3 | 2
4 | 5 | 7 | 6
12 | 13 | 15 | 14
8 | 9 | 11 | 10
D, E
00
01
11
10
B, C
00
01
11
10
16 | 17 | 19 | 18
20 | 21 | 23 | 22
28 | 29 | 31 | 30
24 | 25 | 27 | 26
D, E
00
01
11
10
B, C
00
01
11
10
A = 0
A = 1
Cell 0 can be considered to be ‘adjacent’ to cell 16, cell 1 can be considered to be adjacent to cell 17, and so on.

## Slide 55: Simplification of 5-Variable K-Maps
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
Or
F(A, B, C, D, E)= m1, m2, m3, m5, m7, m11, m13, m17, m19, m23, m29, m31

## Slide 56: Simplification of 5-Variable K-Maps: Step 1
0 | 1 | 1 | 1
0 | 1 | 1 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
D, E
00
01
11
10
B, C
00
01
11
10
0 | 1 | 1 | 0
0 | 0 | 1 | 0
0 | 1 | 1 | 0
0 | 0 | 0 | 0
D, E
00
01
11
10
B, C
00
01
11
10
A = 0
A = 1
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)

## Slide 57: Simplification of 5-Variable K-Maps: Step 2
54
0 | 1 | 1 | 1
0 | 1 | 1 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
D, E
00
01
11
10
B, C
00
01
11
10
0 | 1 | 1 | 0
0 | 0 | 1 | 0
0 | 1 | 1 | 0
0 | 0 | 0 | 0
D, E
00
01
11
10
B, C
00
01
11
10
A = 0
A = 1
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
A’B’E

## Slide 58: Simplification of 5-Variable K-Maps: Step 3
55
D, E
00 | 01 | 11 | 10
0 | 1 | 1 | 1
0 | 1 | 1 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
B, C
00
01
11
10
0 | 1 | 1 | 0
0 | 0 | 1 | 0
0 | 1 | 1 | 0
0 | 0 | 0 | 0
D, E
00
01
11
10
B, C
00
01
11
10
A = 0
A = 1
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
A’B’E+ A’B’C’D

## Slide 59: Simplification of 5-Variable K-Maps: Step 4
56
D, E
00 | 01 | 11 | 10
0 | 1 | 1 | 1
0 | 1 | 1 | 0
0 | 1 | 0 | 0
0 | 0 | 1 | 0
B, C
00
01
11
10
0 | 1 | 1 | 0
0 | 0 | 1 | 0
0 | 1 | 1 | 0
0 | 0 | 0 | 0
D, E
00
01
11
10
B, C
00
01
11
10
A = 0
A = 1
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
A’B’E+ A’B’C’D+A’CD’E

## Slide 60: Simplification of 5-Variable K-Maps: Step 5
57
0
1
1
1
0
1
1
0
0
1
0
0
0
0
1
0
D, E
00
01
11
10
B, C
00
01
11
10
0 | 1 | 1 | 0
0 | 0 | 1 | 0
0 | 1 | 1 | 0
0 | 0 | 0 | 0
D, E
00
01
11
10
B, C
00
01
11
10
A = 0
A = 1
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
A’B’E+ A’B’C’D+A’CD’E+A’C’DE

## Slide 61: Simplification of 5-Variable K-Maps: Step 6
58
0
1
1
1
0
1
1
0
0
1
0
0
0
0
1
0
D, E
00
01
11
10
B, C
00
01
11
10
0 | 1 | 1 | 0
0 | 0 | 1 | 0
0 | 1 | 1 | 0
0 | 0 | 0 | 0
D, E
00
01
11
10
B, C
00
01
11
10
A = 0
A = 1
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
A’B’E+ A’B’C’D+A’CD’E+A’C’DE
AB’DE

## Slide 62: Simplification of 5-Variable K-Maps: Step 7
59
0
1
1
1
0
1
1
0
0
1
0
0
0
0
1
0
D, E
00
01
11
10
B, C
00
01
11
10
0
1
1
0
0
0
1
0
0
1
1
0
0
0
0
0
D, E
00
01
11
10
B, C
00
01
11
10
A = 0
A = 1
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
A’B’E+ A’B’C’D+A’CD’E+A’C’DE
AB’DE+ABCE

## Slide 63: Simplification of 5-Variable K-Maps: Step 8
60
0
1
1
1
0
1
1
0
0
1
0
0
0
0
1
0
D, E
00
01
11
10
B, C
00
01
11
10
0
1
1
0
0
0
1
0
0
1
1
0
0
0
0
0
D, E
00
01
11
10
B, C
00
01
11
10
A = 0
A = 1
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
A’B’E+ A’B’C’D+A’CD’E+A’C’DE
B’C’E
AB’DE+ABCE

## Slide 64: Simplification of 5-Variable K-Maps: Solution
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
F = A’B’E+ A’B’C’D+A’CD’E+A’C’DE+B’C’E+AB’DE+ABCE

## Slide 65: Alternative Representations of 5-Variable K-Maps
Reflection Maps Overlay Maps

## Slide 66: 5-Variable Reflection K-Map
00
01
11
10
0 | 1 | 3 | 2 | 6 | 7 | 5 | 4
8 | 9 | 11 | 10 | 14 | 15 | 13 | 12
24 | 25 | 27 | 26 | 30 | 31 | 29 | 28
16 | 17 | 19 | 18 | 22 | 23 | 21 | 20
C, D, E
000 001 011 010 110 111 101 100
A, B
Think of this line as a mirror

## Slide 67: Simplification of Reflection Map: Step 1
00
01
11
10
0 | 1 | 1 | 1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 0 | 1 | 0 | 0
000 001 011 010 110 111 101 100
A, B
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
C, D, E

## Slide 68: Simplification of Reflection Map: Step 2
10
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
C, D, E
A, B
 | 000 | 001 | 011 | 010 | 110 | 111 | 101 | 100
00 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0
01 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
11 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
B’C’E
0
1
1
0
0
1
0
0

## Slide 69: Simplification of Reflection Map: Step 3
10
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
C, D, E
A, B
 | 000 | 001 | 011 | 010 | 110 | 111 | 101 | 100
00 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0
01 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
11 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0
1
1 0 0 1
B’C’E+A’B’C’D
0
0

## Slide 70: Simplification of Reflection Map: Step 4
A, B
00
01
11
10
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
C, D, E
000 001 011 010 110 111 101 100
0 1 1 1 0 1 1 0
0 0 1 0 0 0 1 0
0 0 0 0 0 1 1 0
0 1 1 0 0 1 0 0
B’C’E+A’B’C’D+A’C’DE

## Slide 71: Simplification of Reflection Map: Step 5
A, B
00
01
11
10
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
C, D, E
000 001 011 010 110 111 101 100
0 1 1 1 0 1 1 0
0 0 1 0 0 0 1 0
0 0 0 0 0 1 1 0
0 1 1 0 0 1 0 0
B’C’E+A’B’C’D+A’C’DE+ABCE

## Slide 72: Simplification of Reflection Map: Step 6
A, B
00
01
11
10
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
C, D, E
000 001 011 010 110 111 101 100
0 1 1 1 0 1 1 0
0 0 1 0 0 0 1 0
0 0 0 0 0 1 1 0
0 1 1 0 0 1 0 0
B’C’E+A’B’C’D+A’C’DE+ABCE+A’B’E

## Slide 73: Simplification of Reflection Map: Step 7
A, B
00
01
11
10
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
C, D, E
000 001 011 010 110 111 101 100
0 1 1 1 0 1 1 0
0 0 1 0 0 0 1 0
0 0 0 0 0 1 1 0
0 1 1 0 0 1 0 0
B’C’E+A’B’C’D+A’C’DE+ABCE+A’B’E+A’CD’E
70

## Slide 74: Simplification of Reflection Map: Step 8
A, B
00
01
11
10
F(A, B, C, D, E) = Σ (1, 2, 3, 5, 7, 11, 13, 17, 19, 23, 29, 31)
C, D, E
000 001 011 010 110 111 101 100
0 1 1 1 0 1 1 0
0 0 1 0 0 0 1 0
0 0 0 0 0 1 1 0
0 1 1 0 0 1 0 0
B’C’E+A’B’C’D+A’C’DE+ABCE+A’B’E+A’CD’E+AB’DE

## Slide 75: Overlay Maps?

## Slide 76: 5-Variable Overlay K-Map
00
01
11
10
0 | 1 | 3 | 2 | 4 | 5 | 7 | 6
8 | 9 | 11 | 10 | 12 | 13 | 15 | 14
24 | 25 | 27 | 26 | 28 | 29 | 31 | 30
16 | 17 | 19 | 18 | 20 | 21 | 23 | 22
C, D, E
000 001 011 010 100 101 111 110
A, B

## Slide 77: 5-Variable Reflection K-Map
5-Variable Overlay K-Map
00
01
11
10
0 | 1 | 3 | 2 | 6 | 7 | 5 | 4
8 | 9 | 11 | 10 | 14 | 15 | 13 | 12
24 | 25 | 27 | 26 | 30 | 31 | 29 | 28
16 | 17 | 19 | 18 | 22 | 23 | 21 | 20
C, D, E
000 001 011 010 110 111 101 100
A, B
00
01
11
10
Reflection maps use the ‘Gray Code’
0 | 1 | 3 | 2 | 4 | 5 | 7 | 6
8 | 9 | 11 | 10 | 12 | 13 | 15 | 14
24 | 25 | 27 | 26 | 28 | 29 | 31 | 30
16 | 17 | 19 | 18 | 20 | 21 | 23 | 22
C, D, E
000 001 011 010 100 101 111 110
A, B

## Slide 78: Simplification of Overlay Map
00
01
11
10
0 | 0 | 1 | 0 | 0 | 1 | 1 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 0 | 0
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1
000 001 011 010 100 101 111 110
A, B
F(A, B, C, D, E) = Σ (3, 5, 6, 7, 9, 10, 11, 12, 13, 14, 17, 18,
19, 20, 21, 22, 24, 25, 26, 28)
C, D, E

## Slide 79: Simplification of Overlay Map
0
0
1
0
0
1
1
1
0
1
1
1
1
1
0
1
1
1
0
1
1
0
0
0
0
1
1
1
1
1
0
1
000 001 011 010 100 101 111 110
A, B
00
01
11
10
F(A, B, C, D, E) = Σ (3, 5, 6, 7, 9, 10, 11, 12, 13, 14, 17, 18, 19, 20, 21, 22, 24, 25, 26, 28)
C, D, E

## Slide 80: 5-Variable K-Map with Don’t Care Conditions
F(A, B, C, D, E)= Σ(1, 2, 3, 8, 9, 10, 12, 15, 16, 17, 18, 22, 26, 27)
+d(0, 4, 11, 19, 28, 30, 31)
x | 1 | 1 | 1
x | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | x | 1
D, E
00
01
11
10
B, C
00
01
11
10
1 | 1 | x | 1
0 | 0 | 0 | 1
x | 0 | x | x
0 | 0 | 1 | 1
D, E
00
01
11
10
B, C
00
01
11
10
A = 0
A = 1

## Slide 81: Homework
Simplify the following Boolean function:
F(A,B,C,D,E)=Σ(0, 1, 2, 3, 8, 12, 15, 16, 17, 18, 19, 22, 28, 31)

## Slide 82: K-Maps with Don’t Care Conditions
1 | x | x | 1
0 | x | 1 | 0
Sometimes, we have function where it doesn’t matter whether the output is 0 or 1; it can be either.
These are known as ‘DON’T CARE CONDITIONS’. Such conditions are marked with an ‘x’ in the map.
B, C
00 01 11 10
A
0
1
F(A, B, C)= Σ(0, 2, 7)+d(1, 3, 5 )

## Slide 83: Map Simplification in the Presence of Don’t Care Conditions
1 | x | x | 1
0 | x | 1 | 0
B, C
00
01
11
10
A
0
1
F= A’+C

## Slide 84: Combinational Circuits

## Slide 85: Combinational Circuits
A combinational circuit is a connected arrangement of logic gates with a set of inputs and outputs.
Combinational Circuits
Half Adder
Full Adder

## Slide 86: Adders
Addition is the most basic digital arithmetic operation.
A combinational circuit that adds two bits is called a HALF-ADDER
and
the one that adds three bits (i.e., two significant bits and a previous carry) is called a FULL-ADDER.

## Slide 87: Half-Adder
S (sum)= A’B+AB’= A⊕B
C (carry)= AB
Truth Table
Logic Diagram

## Slide 88: Full-Adder
S (sum)= A⊕B⊕Cin
Cout (carry)= AB+(A+B)Cin
Truth Table
Logic Diagram

## Slide 90: Homework 1
Simplify the following Boolean functions:
F(A,B,C,D)=Σ(1, 3, 7, 8, 9, 12, 13, 14, 15)
F(A,B,C,D)=Π(0, 2, 4, 5, 8, 10, 12, 13)

## Slide 91: Homework 2
Given the following Boolean function:
F=x+x’y’
List the truth table
Draw the logic circuit

## Slide 92
Boolean Function Truth Table |  |  |  |  |  | 
F = x + x’ y’ | x | y | x’ | y’ | x’y’ | x+x’y’ (=F)

## Slide 93: In the next lecture, we will study…
Flip – Flops
Sequential circuits
Decoders
Multiplexers
Registers