## Slide 1: Multiplexer and Demultiplexer

## Slide 2: Multiplexer
A multiplexer is a combinational circuit that has 2n input lines and a single output line. Simply, the multiplexer is a multi-input and single-output combinational circuit. The binary information is received from the input lines and directed to the output line. On the basis of the values of the selection lines, one of these data inputs will be connected to the output.
Unlike encoder and decoder, there are n selection lines and 2n input lines. So, there is a total of 2N possible combinations of inputs. A multiplexer is also treated as Mux.
There are various types of the multiplexer which are as follows:
2×1 Multiplexer
4×1 Multiplexer
8 to 1 Multiplexer
16 to 1 Multiplexer

## Slide 3: 2×1 Multiplexer
In 2×1 multiplexer, there are only two inputs, i.e., A0 and A1, 1 selection line, i.e., S0 and single outputs, i.e., Y. On the basis of the combination of inputs which are present at the selection line S0, one of these 2 inputs will be connected to the output.

## Slide 4: 2×1 Multiplexer
Truth Table:
The logical expression of the term Y is as follows:
Y=S0'.A0 + S0.A1
Block Diagram:
Logical circuit:

## Slide 5: 4×1 Multiplexer
In the 4×1 multiplexer, there is a total of four inputs, i.e., A0, A1, A2, and A3, 2 selection lines, i.e., S0 and S1 and single output, i.e., Y. On the basis of the combination of inputs that are present at the selection lines S0 and S1, one of these 4 inputs are connected to the output.

## Slide 6: 4×1 Multiplexer
Truth Table:
Block Diagram:
Logical circuit:
The logical expression of the term Y is as follows:
Y=S1' S0' A0 + S1' S0 A1 + S1 S0' A2 + S1 S0 A3

## Slide 7: 8×1 Multiplexer
In the 8 to 1 multiplexer, there are total eight inputs, i.e., A0, A1, A2, A3, A4, A5, A6, and A7, 3 selection lines, i.e., S0, S1and S2 and single output, i.e., Y. On the basis of the combination of inputs that are present at the selection lines S0, S1, and S2, one of these 8 inputs are connected to the output.

## Slide 8: 8×1 Multiplexer
Truth Table:
Block Diagram:
Logical circuit:
The logical expression of the term Y is as follows:
Y=S0'.S1'.S2'.A0 + S0.S1'.S2'.A1 + S0'.S1.S2'.A2 + S0.S1.S2'.A3 + S0'.S1'.S2 A4 + S0.S1'.S2 A5 + S0'.S1.S2 .A6 + S0.S1.S3.A7

## Slide 9: 8×1 Multiplexer using 4×1 and 2×1 multiplexer
We can implement the 8×1 multiplexer using a lower order multiplexer. To implement the 8×1 multiplexer, we need two 4×1 multiplexers and one 2×1 multiplexer. The 4×1 multiplexer has 2 selection lines, 4 inputs, and 1 output. The 2×1 multiplexer has only 1 selection line.
For getting 8 data inputs, we need two 4×1 multiplexers. The 4×1 multiplexer produces one output. So, in order to get the final output, we need a 2×1 multiplexer.

## Slide 10: 8×1 Multiplexer using 4×1 and 2×1 multiplexer
Block Diagram:

## Slide 11: 16×1 Multiplexer
In the 16 to 1 multiplexer, there are total of 16 inputs, i.e., A0, A1, …, A16, 4 selection lines, i.e., S0, S1, S2, and S3 and single output, i.e., Y. On the basis of the combination of inputs that are present at the selection lines S0, S1, and S2, one of these 16 inputs will be connected to the output.

## Slide 12: 16×1 Multiplexer
Truth Table:
Block Diagram:
Logical circuit:
The logical expression of the term Y is as follows:
Y=A0.S0'.S1'.S2'.S3‘ + A1.S0'.S1'.S2 '.S3 + A2.S0'.S1'.S2.S3‘ + A3.S0'.S1 '.S2.S3 + A4.S0'.S1.S2'.S3‘ + A5.S0'.S1.S2'.S3 + A6.S1.S2.S3‘ + A7.S0'.S1.S2.S3 + A8.S0.S1'.S2'.S3‘ + A9.S0.S1'.S2'.S3 + Y10.S0.S1'.S2.S3 ‘ + A11.S0.S1'.S2.S3 + A12 S0.S1.S2 '.S3‘ + A13.S0.S1.S2'.S3 + A14.S0.S1 .S2.S3‘ + A15.S0.S1.S2'.S3

## Slide 13: 16×1 Multiplexer using 8×1 and 2×1 multiplexer
We can implement the 16×1 multiplexer using a lower order multiplexer. To implement the 8×1 multiplexer, we need two 8×1 multiplexers and one 2×1 multiplexer. The 8×1 multiplexer has 3 selection lines, 4 inputs, and 1 output. The 2×1 multiplexer has only 1 selection line.
For getting 16 data inputs, we need two 8 ×1 multiplexers. The 8×1 multiplexer produces one output. So, in order to get the final output, we need a 2×1 multiplexer.

## Slide 14: 16×1 Multiplexer using 8×1 and 2×1 multiplexer
Block Diagram:

## Slide 15: De-multiplexer
A De-multiplexer is a combinational circuit that has only 1 input line and 2N output lines. Simply, the de-multiplexer is a single-input and multi-output combinational circuit. The information is received from the single input lines and directed to the output line. On the basis of the values of the selection lines, the input will be connected to one of these outputs. De-multiplexer is opposite to the multiplexer.
Unlike encoder and decoder, there are n selection lines and 2n outputs. So, there is a total of 2n possible combinations of inputs. De-multiplexer is also treated as De-mux.
There are various types of the De-multiplexer which are as follows:
1×2 De-multiplexer
1×4 De-multiplexer
1×8 De-multiplexer
1×16 De-multiplexer

## Slide 16: 1×2 De-multiplexer
In the 1 to 2 De-multiplexer, there are only two outputs, i.e., Y0, and Y1, 1 selection lines, i.e., S0, and single input, i.e., A. On the basis of the selection value, the input will be connected to one of the outputs.

## Slide 17: 1×2 De-multiplexer
Truth Table:
The logical expression of the term Y is as follows:
Y0=S0'.A Y1=S0.A
Block Diagram:
Logical circuit:

## Slide 18: 1×4 De-multiplexer
In 1 to 4 De-multiplexer, there are total of four outputs, i.e., Y0, Y1, Y2, and Y3, 2 selection lines, i.e., S0 and S1 and single input, i.e., A. On the basis of the combination of inputs which are present at the selection lines S0 and S1, the input be connected to one of the outputs.

## Slide 19: 1×4 De-multiplexer
Truth Table:
Block Diagram:
Logical circuit:
The logical expression of the term Y is as follows:
Y0=S1' S0' A y1=S1' S0 A y2=S1 S0' A y3=S1 S0 A

## Slide 20: 1×8 De-multiplexer
In 1 to 8 De-multiplexer, there are total of eight outputs, i.e., Y0, Y1, Y2, Y3, Y4, Y5, Y6, and Y7, 3 selection lines, i.e., S0, S1and S2 and single input, i.e., A. On the basis of the combination of inputs which are present at the selection lines S0, S1 and S2, the input will be connected to one of these outputs.

## Slide 21: 1×8 De-multiplexer
Truth Table:
Block Diagram:
Logical circuit:
The logical expression of the term Y is as follows:
Y0=S0'.S1'.S2'.A Y1=S0.S1'.S2'.A Y2=S0'.S1.S2'.A Y3=S0.S1.S2'.A Y4=S0'.S1'.S2 A Y5=S0.S1'.S2 A Y6=S0'.S1.S2 A Y7=S0.S1.S3.A

## Slide 22: 1×8 De-multiplexer using 1×4 and 1×2 De-multiplexer
We can implement the 1×8 de-multiplexer using a lower order de-multiplexer. To implement the 1×8 de-multiplexer, we need two 1×4 de-multiplexer and one 1×2 de-multiplexer. The 1×4 multiplexer has 2 selection lines, 4 outputs, and 1 input. The 1×2 de-multiplexer has only 1 selection line.
For getting 8 data outputs, we need two 1×4 de-multiplexer. The 1×2 de-multiplexer produces two outputs. So, in order to get the final output, we have to pass the outputs of 1×2 de-multiplexer as an input of both the 1×4 de-multiplexer.

## Slide 23: 1×8 De-multiplexer using 1×4 and 1×2 De-multiplexer
Block Diagram:

## Slide 24: 1×16 De-multiplexer
In 1×16 de-multiplexer, there are total of 16 outputs, i.e., Y0, Y1, …, Y16, 4 selection lines, i.e., S0, S1, S2, and S3 and single input, i.e., A. On the basis of the combination of inputs which are present at the selection lines S0, S1, and S2, the input will be connected to one of these outputs.

## Slide 25: 1×16 De-multiplexer
Truth Table:
Block Diagram:
Logical circuit:
The logical expression of the term Y is as follows:
Y0=A.S0'.S1'.S2'.S3‘ Y1=A.S0'.S1'.S2'.S3 Y2=A.S0'.S1'.S2.S3‘ Y3=A.S0'.S1'.S2.S3 Y4=A.S0'.S1.S2'.S3‘ Y5=A.S0'.S1.S2'.S3 Y6=A.S0'.S1.S2.S3‘ Y7=A.S0'.S1.S2.S3 Y8=A.S0.S1'.S2'.S3‘ Y9=A.S0.S1'.S2'.S3 Y10=A.S0.S1'.S2.S3‘ Y11=A.S0.S1'.S2.S3 Y12=A.S0.S1.S2'.S3‘ Y13=A.S0.S1.S2'.S3 Y14=A.S0.S1.S2.S3‘ Y15=A.S0.S1.S2'.S3

## Slide 26: 1×16 De-multiplexer using 1×8 and 1×2 De-multiplexer
We can implement the 1×16 de-multiplexer using a lower order de-multiplexer. To implement the 1×16 de-multiplexer, we need two 1×8 de-multiplexer and one 1×2 de-multiplexer. The 1×8 multiplexer has 3 selection lines, 1 input, and 8 outputs. The 1×2 de-multiplexer has only 1 selection line.
For getting 16 data outputs, we need two 1×8 de-multiplexer. The 1×8 de-multiplexer produces eight outputs. So, in order to get the final output, we need a 1×2 de-multiplexer to produce two outputs from a single input. Then we pass these outputs into both the de-multiplexer as an input.

## Slide 27: 1×16 De-multiplexer using 1×8 and 1×2 De-multiplexer
Block Diagram: