## Slide 1: Decoder and Encoder

## Slide 2: Decoder
The combinational circuit that change the binary information into 2N output lines is known as Decoders. The binary information is passed in the form of N input lines. The output lines define the 2N N-bit code for the binary information. In simple words, the Decoder performs the reverse operation of the Encoder. At a time, only one output line is activated for simplicity. The produced 2N-bit output code is equivalent to the binary information. There are various types of decoders which are as follows:

## Slide 3: 2 to 4 line Decoder
In the 2 to 4 line decoder, there is a total of three inputs, i.e., A0, and A1 and E and four outputs, i.e., Y0, Y1, Y2, and Y3. For each combination of inputs, when the enable 'E' is set to 1, one of these four outputs will be 1. The block diagram and the truth table of the 2 to 4 line decoder are given below.

## Slide 4: 2 to 4 line Decoder
Truth Table:
The logical expression of the term Y0, Y1, Y2, and Y3 is as follows:
Y3=E.A1.A0 Y2=E.A1.A0'
Y1=E.A1'.A0 Y0=E.A1'.A0'
Block Diagram:
Logical circuit:

## Slide 5: 3 to 8 line decoder
The 3 to 8 line decoder is also known as Binary to Octal Decoder. In a 3 to 8 line decoder, there is a total of eight outputs, i.e., Y0, Y1, Y2, Y3, Y4, Y5, Y6, and Y7 and three inputs, i.e., A0, A1, and A2. This circuit has an enable input 'E'. Just like 2 to 4 line decoder, when enable 'E' is set to 1, one of these four outputs will be 1. The block diagram and the truth table of the 3 to 8 line encoder are given below.

## Slide 6: 3 to 8 line decoder
Truth Table:
Block Diagram:
Logical circuit:
The logical expression of the term Y0, Y1, Y2, Y3, Y4, Y5, Y6, and Y7 is as follows:
Y0=A0'.A1'.A2’ Y1=A0.A1'.A2’ Y2=A0'.A1.A2’ Y3=A0.A1.A2’ Y4=A0'.A1'.A2 Y5=A0.A1'.A2 Y6=A0'.A1.A2 Y7=A0.A1.A2
E

## Slide 7: 4 to 16 line decoder
In the 4 to 16 line decoder, there is a total of 16 outputs, i.e., Y0, Y1, Y2,……, Y15 and four inputs, i.e., A0, A1, A2, and A3. The 4 to 16 line decoder can be constructed using either 2 to 4 decoder or 3 to 8 decoder. There is the following formula used to find the required number of lower-order decoders.
Required number of lower order decoders=m2/m1
m1 = 8 m2 = 16
Required number of 3 to 8 decoders= =2

## Slide 8: 4 to 16 line decoder
Truth Table:
Block Diagram:
Logical circuit:
The logical expression of the term Y0, Y1, Y2,…, Y15 are as follows:
Y0=A0'.A1'.A2'.A3’ Y1=A0'.A1'.A2'.A3 Y2=A0'.A1'.A2.A3‘ Y3=A0'.A1'.A2.A3 Y4=A0'.A1.A2'.A3‘ Y5=A0'.A1.A2'.A3 Y6=A0'.A1.A2.A3‘ Y7=A0'.A1.A2.A3 Y8=A0.A1'.A2'.A3‘ Y9=A0.A1'.A2'.A3 Y10=A0.A1'.A2.A3‘ Y11=A0.A1'.A2.A3 Y12=A0.A1.A2'.A3‘ Y13=A0.A1.A2'.A3 Y14=A0.A1.A2.A3' Y15=A0.A1.A2'.A3

## Slide 9: Encoder
The combinational circuits that change the binary information into N output lines are known as Encoders. The binary information is passed in the form of 2N input lines. The output lines define the N-bit code for the binary information. In simple words, the Encoder performs the reverse operation of the Decoder. At a time, only one input line is activated for simplicity. The produced N-bit output code is equivalent to the binary information. There are various types of encoders which are as follows:

## Slide 10: 4 to 2 line Encoder
In 4 to 2 line encoder, there are total of four inputs, i.e., Y0, Y1, Y2, and Y3, and two outputs, i.e., A0 and A1. In 4-input lines, one input-line is set to true at a time to get the respective binary code in the output side. Below are the block diagram and the truth table of the 4 to 2 line encoder.

## Slide 11: 4 to 2 line Encoder
Truth Table:
The logical expression of the term A0 and A1 is as follows:
A1=Y3+Y2 A0=Y3+Y1
Block Diagram:
Logical circuit:

## Slide 12: 8 to 3 line Encoder
The 8 to 3 line Encoder is also known as Octal to Binary Encoder. In 8 to 3 line encoder, there is a total of eight inputs, i.e., Y0, Y1, Y2, Y3, Y4, Y5, Y6, and Y7 and three outputs, i.e., A0, A1, and A2. In 8-input lines, one input-line is set to true at a time to get the respective binary code in the output side. Below are the block diagram and the truth table of the 8 to 3 line encoder.

## Slide 13: 8 to 3 line Encoder
Truth Table:
Block Diagram:
Logical circuit:
The logical expression of the term A0, A1, and A2 are as follows:
A2=Y4+Y5+Y6+Y7 A1=Y2+Y3+Y6+Y7 A0=Y7+Y5+Y3+Y1