## Slide 1: MEMORY ORGANIZATION
1
Memory Hierarchy
Main Memory
Auxiliary Memory
Associative Memory
Cache Memory
Virtual Memory
Memory Management Hardware

## Slide 2
2
Memory Organization
MEMORY HIERARCHY
Magnetic
tapes
Magnetic
disks
I/O processor
CPU
Main memory
Cache memory
Auxiliary memory
Register
Cache
Main Memory
Magnetic Disk
Magnetic Tape
Memory Hierarchy is to obtain the highest possible
access speed while minimizing the total cost of the memory system
Memory Hierarchy

## Slide 3
3
Memory Organization
MAIN MEMORY
RAM and ROM Chips
Typical RAM chip
Typical ROM chip
Chip select 1
Chip select 2
Read
Write 7-bit address
 | CS1 CS2 RD 128 x 8 WR RAM AD 7
8-bit data bus
CS1 | CS2 | RD | WR | Memory function | State of data bus
0 | 0 | x | x | Inhibit | High-impedence
0 | 1 | x | x | Inhibit | High-impedence
1 1 | 0 0 | 0 0 | 0 1 | Inhibit Write | High-impedence Input data to RAM
1 1 | 0 1 | 1 x | x x | Read Inhibit | Output data from RAM High-impedence
Chip select 1
Chip select 2
9-bit address
CS1
CS2
AD 9
512 x 8
ROM
8-bit data bus
Main Memory
Types of Memory
Static
Dynamic
Uses of ROM
Bootstrap Loader
Computer Startup

## Slide 4
4
Memory Organization
Component | Hexa | Address bus |  |  |  |  |  |  |  |  | 
 | address | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1
RAM 1 | 0000 - 007F | 0 0 0 0 1 | 0 0 1 1 x | 0 1 0 1 x | x x x x x | x x x x x | x x x x x | x x x x x | x x x x x | x x x x x | x x x x x
RAM 2 | 0080 - 00FF |  |  |  |  |  |  |  |  |  | 
RAM 3 | 0100 - 017F |  |  |  |  |  |  |  |  |  | 
RAM 4 | 0180 - 01FF |  |  |  |  |  |  |  |  |  | 
ROM | 0200 - 03FF |  |  |  |  |  |  |  |  |  | 
Memory Connection to CPU
- RAM and ROM chips are connected to a CPU
through the data and address buses
- The low-order lines in the address bus select the byte within the chips and other lines in the address bus select a particular chip through its chip select inputs
MEMORY ADDRESS MAP
Address space assignment to each memory chip
Example: 512 bytes RAM and 512 bytes ROM
Main Memory

## Slide 5
5
Memory Organization
CONNECTION OF MEMORY TO CPU
Main Memory

## Slide 6
6
Memory Organization
AUXILIARY MEMORY
EOF
block 3
block 1
block 2
R1 R2
R3 R4
R5
R6
R1
R3 R2
block 3 IRG
R5 R4
Information Organization on Magnetic Tapes
file i
block 1 block 2
EOF
Track
Organization of Disk Hardware
Moving Head Disk
Fixed Head Disk
Auxiliary Memory
Access Time
Seek Time
Transfer Time
Characteristics of Auxiliary Memory
Access Mode
Access Time
Transfer rate
Capacity
Cost

## Slide 7
Memory Organization
7
ASSOCIATIVE MEMORY
Accessed by the content of the data rather than by an address
Also called Content Addressable Memory (CAM)
Hardware Organization
Argument register(A)
Key register (K)
Associative memory array and logic
m words
n bits per word
Match register
Input
Read
Write
M
Compare each word in CAM in parallel with the
content of A(Argument Register)
  If CAM Word[i] = A, M(i) = 1
  Read sequentially accessing CAM for CAM Word(i) for M(i) = 1
K(Key Register) provides a mask for choosing a particular field or key in the argument in A (only those bits in the argument that have 1’s in
their corresponding position of K are compared)
Associative Memory
A:
K:
101 111100
111 000000
Word 1: 100 111100 (No Match)
Word 2: 101 000001 (Match)

## Slide 8
8
Memory Organization
ORGANIZATION OF CAM
Associative Memory

## Slide 9
9
Memory Organization
MATCH
LOGIC
Associative Memory
𝒋 𝒊𝒋
𝒙𝒋 = 𝑨𝒋𝑭𝒊𝒋 + 𝑨′𝑭′
𝑴𝒊 = 𝒙𝟏𝒙𝟐𝒙𝟑 … 𝒙𝒏

## Slide 10
10
Memory Organization
MATCH
LOGIC
Associative Memory
F'i1
F i1
K1
A1
F'i2
F i2
K2
A2
F'in Fin
Kn
An
. . . .
M i

## Slide 11
11
Memory Organization
CACHE MEMORY
Locality of Reference
The references to memory at any given time
interval tend to be confined within a localized areas
This area contains a set of information and
the membership changes gradually as time goes by
Temporal Locality
The information which will be used in near future
is likely to be in use already( e.g. Reuse of information in loops)
Spatial Locality
If a word is accessed, adjacent(near) words are likely accessed soon (e.g. Related data items (arrays) are usually stored together; instructions are executed sequentially)
Cache
The property of Locality of Reference makes the
Cache memory systems work
Cache is a fast small capacity memory that should hold those information which are most likely to be accessed
Cache Memory
Main memory
Cache memory
CPU

## Slide 12
12
Memory Organization
How can we know if the word that is required
is there ?
If a new block is to replace one of the old blocks, which one should we choose ?
PERFORMANCE OF CACHE
Memory Access
All the memory accesses are directed first to Cache
If the word is in Cache; Access cache to provide it to CPU
If the word is not in Cache; Bring a block (or a line) including
that word to replace a block now in Cache
Performance of Cache Memory System
Hit Ratio - % of memory accesses satisfied by Cache memory system Te: Effective memory access time in Cache memory system
Tc: Cache access time
Tm: Main memory access time
Te = Tc + (1 - h) Tm
Example: Tc = 0.4 s, Tm = 1.2s, h = 0.85
Te = 0.4 + (1 - 0.85) * 1.2 = 0.58s
Cache Memory

## Slide 13
12
Memory Organization
MEMORY AND CACHE | MAPPING - ASSOCIATIVE MAPPLING - |  | 
Mapping Function Specification of correspondence between main memory blocks and cache blocks Associative mapping Direct mapping Set-associative mapping Associative Mapping Any block location in Cache can store any block in memory -> Most flexible Mapping Table is implemented in an associative memory -> Fast, very Expensive Mapping Table Stores both address and the content of the memory word address (15 bits) Argument register Address Data |  |  | 
CAM | 0 1 0 0 0 | 3 4 5 0 | 
 | 0 2 7 7 7 | 6 7 1 0 | 
 | 2 2 2 3 5 | 1 2 3 4 | 
Cache Memory

## Slide 14
13
Memory Organization
Cache Memory
MEMORY AND CACHE MAPPING-DIRECT MAPPING
-Each memory block has only one place to load in Cache
-Mapping Table is made of RAM instead of CAM
-n-bit memory address consists of 2 parts' bits of Index field and n-k bits of Tag field
-n-bit addresses are used to access main memory and k-bit Index is used to access the Cache

## Slide 15
14
Memory Organization
DIRECT MAPPING
000 007 | 0 1 0 1 | 3 4 5 0 6 5 7 8
010 017 |  | 
770 777 | 0 2 0 2 | 6 7 1 0
Block 63
Tag | Block | Word
Operation
CPU generates a memory request with (TAG;INDEX)
Access Cache using INDEX ; (tag;
data) Compare TAG and tag
If matches -> Hit
Provide Cache[INDEX](data) to CPU
If not match -> Miss
M[tag;INDEX] <- Cache[INDEX](data)
Cache[INDEX] <- (TAG;M[TAG; INDEX])
CPU <- Cache[INDEX](data)
Direct Mapping with block size of 8 words
Index tag data 6
6
3
Block 0
INDEX
Block 1
Cache Memory

## Slide 16: MEMORY AND CACHE MAPPING - SET ASSOCIATIVE MAPPING -
Memory Organization 15 Cache Memory
- Each memory block has a set of locations in the Cache to load
Set Associative Mapping Cache with set size of two
Operation
CPU generates a memory address(TAG; INDEX)
Access Cache with INDEX, (Cache word = (tag 0, data 0); (tag 1, data 1))
Compare TAG and tag 0 and then tag 1
If tag i = TAG -> Hit, CPU <- data i
If tag i  TAG -> Miss,
Replace either (tag 0, data 0) or (tag 1, data 1), Assume (tag 0, data 0) is selected for replacement, (Why (tag 0, data 0) instead of (tag 1, data 1) ?)
M[tag 0, INDEX] <- Cache[INDEX](data 0) Cache[INDEX](tag 0, data 0) <- (TAG, M[TAG,INDEX]),
CPU <- Cache[INDEX](data 0)

## Slide 17
16
Memory Organization
BLOCK REPLACEMENT POLICY
Many different block replacement policies are available
LRU(Least Recently Used) is most easy to implement
Cache word = (tag 0, data 0, U0);(tag 1, data 1, U1), Ui = 0 or 1(binary)
Implementation of LRU in the Set Associative Mapping with set size = 2
Modifications
Initially all U0 = U1 = 1
When Hit to (tag 0, data 0, U0), U1 <- 1(least recently used) (When Hit to (tag 1, data 1, U1), U0 <- 1(least recently used)) When Miss, find the least recently used one(Ui=1)
If U0 = 1, and U1 = 0, then replace (tag 0, data 0)
M[tag 0, INDEX] <- Cache[INDEX](data 0)
Cache[INDEX](tag 0, data 0, U0) <- (TAG,M[TAG,INDEX], 0); U1 <- 1
If U0 = 0, and U1 = 1, then replace (tag 1, data 1)
Similar to above; U0 <- 1
If U0 = U1 = 0, this condition does not exist If U0 = U1 = 1, Both of them are candidates,
Take arbitrary selection
Cache Memory

## Slide 18
17
Memory Organization
CACHE WRITE
Write Through
When writing into memory
If Hit, both Cache and memory is written in parallel
If Miss, Memory is written
For a read miss, missing block may be overloaded onto a cache block
Memory is always updated
-> Important when CPU and DMA I/O are both executing
Slow, due to the memory access time
Write-Back (Copy-Back)
When writing into memory
If Hit, only Cache is written
If Miss, missing block is brought to Cache and write into Cache
For a read miss, candidate block must be
written back to the memory
Memory is not up-to-date, i.e., the same item in
Cache and memory may have different value
Cache Memory

## Slide 19
18
Memory Organization
VIRTUAL MEMORY
Give the programmer the illusion that the system has a very large memory,
even though the computer actually has a relatively small main memory
Address Space(Logical) and Memory Space(Physical)
virtual address (logical address)
physical address
address space
memory space
Mapping
Virtual Memory
address generated by programs actual main memory address
Address Mapping
Memory Mapping Table for Virtual Address -> Physical Address
Virtual address
Virtual address register
Memory mapping table
Main memory address register
Main memory
Physical
Address
Memory table
buffer register
Main memory
buffer register

## Slide 20
19
Memory Organization
Organization of memory Mapping Table in a paged system
ADDRESS MAPPING
Address Space and Memory Space are each divided into fixed size group of words called blocks or pages
1K words group
Page 0
Page 1
Page 2
Page 3
Page 4
Page 5
Page 6
Page 7
Block 0
Block 1
Block 2
Block 3
Address space N = 8K = 213
Memory space
M = 4K = 212
000
001
010
011
100
101
110
111
Block 0
Block 1
Block 2
Block 3
MBR
0 1
0 1 0 1 0 1 0 0 1 1
1 0 1
0 1 0 1 0 1 0 0 1 1
Table address
Presence
1
01
bit
Page no. Line number
Virtual address
Main memory address register
Memory page table
Main memory
 |  | 0
11 |  | 1
00 |  | 1
 |  | 0
 |  | 0
01 |  | 1
10 |  | 1
 |  | 0
Virtual Memory

## Slide 21: ASSOCIATIVE MEMORY PAGE TABLE
Memory Organization 20
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
Page no.Block no.
Assume that
Number of Blocks in memory = m
Number of Pages in Virtual Address Space = n
Page Table
- Straight forward design -> n entry table in memory
Inefficient storage space utilization
<- n-m entries of the table is empty
- More efficient method is m-entry Page Table Page Table made of an Associative Memory m words; (Page Number:Block Number)
Virtual address
Page no.
1 0 1 Line number Argument register
1 0 1 0 0 Key register
Associative memory
Page Fault
Page number cannot be found in the Page Table
Virtual Memory

## Slide 22
21
Memory Organization
PAGE FAULT
Processor architecture should provide the ability
to restart any instruction after a page fault.
Trap to the OS
Save the user registers and program state
Determine that the interrupt was a page fault
Check that the page reference was legal and
determine the location of the page on the
backing store(disk)
Issue a read from the backing store to a free
frame
  Wait in a queue for this device until serviced
  Wait for the device seek and/or latency time
  Begin the transfer of the page to a free frame
While waiting, the CPU may be allocated to
some other process
Interrupt from the backing store (I/O completed)
Save the registers and program state for the other user
Determine that the interrupt was from the backing store
Correct the page tables (the desired page is now in memory)
Wait for the CPU to be allocated to this process again
Restore the user registers, program state, and new page table, then resume the interrupted instruction.
3 Page is on backing store
LOAD M
0
1 Reference
OS
trap
2
 | free frame
main memory
4
bring in missing page
5
reset page table
6
restart
instruction
Virtual Memory

## Slide 23
22
Memory Organization
f 0 | v i
f | v
PAGE REPLACEMENT
frame
Decision on which page to displace to make room for an incoming page when no free frame is available
Modified page fault service routine
Find the location of the desired page on the backing store
Find a free frame
  If there is a free frame, use it
  Otherwise, use a page-replacement algorithm to select a victim
  Write the victim page to the backing store
Read the desired page into the (newly) free frame
4. Restart the user process
frame
valid/ invalid bit
page table
2 change to
invalid
4
reset page table for new page
victim
swap out
1 victim
page
3
swap desired page in
backing store
physical memory
Virtual Memory

## Slide 24: PAGE REPLACEMENT ALGORITHMS
Memory Organization 23
FIFO
7
0
7
7
0
1
2
0
1
2
3
1
2
3
0
4
3
0
4
2
0
4
2
3
0
2
3
0
1
3
0
1
2
7
1
2
7
0
2
7
0
1
Page frames
Reference string
7 0 1 2 0 3 0 4 2 3 0 3 2 1 2 0 1 7 0 1
-
FIFO algorithm selects the page that has been in memory the longest time
Using a queue - every time a page is loaded, its
identification is inserted in the queue
Easy to implement
May result in a frequent page fault
Optimal Replacement (OPT) - Lowest page fault rate of all algorithms
Replace that page which will not be used for the longest period of time
1 7 0 1
7
0
7
7
0
1
2
0
1
2
0
3
2
4
3
2
0
3
2
0
1
7
0
1
Page frames
Reference string
7 0 1 2 0 3 0 4 2 3
0 3 2 1 2 0
Virtual Memory

## Slide 25: PAGE REPLACEMENT ALGORITHMS
Memory Organization 24
Replace that page which has not been
used for the longest period of time
LRU
OPT is difficult to implement since it requires future knowledge
LRU uses the recent past as an approximation of near future.
7
0
7
7
0
1
2
0
1
2
0
3
4
0
3
4
0
2
4
3
2
0
3
2
1
3
2
1
0
2
1
0
7
Page frames
Reference string
7 0 1 2 0 3 0 4 2 3 0 3 2 1 2 0 1 7 0 1
Virtual Memory
LRU may require substantial hardware assistance
The problem is to determine an order for the frames
defined by the time of last use

## Slide 26: PAGE REPLACEMENT ALGORITHMS
Memory Organization 25
LRU Approximation
Reference (or use) bit is used to approximate the LRU
Turned on when the corresponding page is
referenced after its initial loading
Additional reference bits may be used
Virtual Memory
2
1
0
7
4
7
2
1
0
4
LRU Implementation Methods
Counters
  For each page table entry - time-of-use register
  Incremented for every memory reference
  Page with the smallest value in time-of-use register is replaced
Stack
  Stack of page numbers
  Whenever a page is referenced its page number is removed from the stack and pushed on top
  Least recently used page number is at the bottom
Reference string
4 7 0 7 1 0 1 2 1 2 7 1 2

## Slide 27: MEMORY MANAGEMENT HARDWARE
Subroutine
Stack
SQRT
Main
Program
Symbol Table
Basic Functions of MM
Dynamic Storage Relocation - mapping logical
memory references to physical memory references
Provision for Sharing common information
stored in memory by different users
Protection of information against unauthorized access
Segmentation
- A segment is a set of logically related instructions or data elements associated with a given name
- Variable size
User's view of memory
User's view of a program
The user does not think of memory as a linear array of words. Rather the user prefers to view memory as a collection of variable sized segments, with no necessary ordering among segments.
Memory Organization 26 Memory Management Hardware

## Slide 28
27
Memory Organization
SEGMENTATION
A memory management scheme which supports
user's view of memory
A logical address space is a collection of segments
Each segment has a name and a length
Address specify both the segment name and the offset within the segment.
For simplicity of implementations, segments are numbered.
Segmentation Hardware
Segment Table
limit
base
(s,d)
s
Memory
+
y
<
n
error
CPU
Memory Management Hardware

## Slide 29: SEGMENTATION EXAMPLE
Memory Organization
Subroutine
Segment 0
Stack
Segment 3
SQRT
Segment 1
Main
Program
Segment 2
Symbol Table
Segment 4
Segment 0
Segment 3
Segment 2
Segment 4
Segment 1
1400
2400
3200
4300
4700
5700
6300
6700
Segment Table
limit | base
1000 400 400 1100 1000 | 1400 6300 4300 3200 4700
0
1
2
3
4
Logical Address Space
28 Memory Management Hardware

## Slide 30: SHARING OF SEGMENTS
Memory Organization
Editor
Segment 0
Data 1
Segment 1
Logical Memory
(User 1)
Editor
Segment 0
Data 2
Segment 1
Logical Memory
(User 2)
43062
68348
72773
90003
98556
Editor
Data 1
Data 2
limit | base
25286 | 43062
4425 | 68348
0
1
Segment Table
(User 1)
limit | base
25286 | 43062
8550 | 90003
0
1
Segment Table (User 2)
Physical Memory
29 Memory Management Hardware

## Slide 31: SEGMENTED PAGE SYSTEM
Memory Organization
Segment
Page
Word
Segment table
Page table
+
Block
Word
Logical address
Physical address
30 Memory Management Hardware

## Slide 32: IMPLEMENTATION OF PAGE AND SEGMENT TABLES
Implementation of the Page Table
Hardware registers (if the page table is reasonably small)
Main memory
  Page Table Base Register(PTBR) points to PT
  Two memory accesses are needed to access
a word; one for the page table, one for the word
- Cache memory (TLB: Translation Lookaside Buffer)
- To speedup the effective memory access time, a special small memory called associative memory, or cache is used
Implementation of the Segment Table Similar to the case of the page table
Memory Organization 31 Memory Management Hardware

## Slide 33
32
Memory Organization
EXAMPLE
Segment | Page | Word
Physical address format: 4096 blocks of 256 words
each, each word has 32bits
12 8
Block Word
220 x 32
Physical
memory
Logical and Physical Addresses
Logical address format: 16 segments of 256 pages
each, each page has 256words
4 8 8
Logical and Physical Memory Address Assignment
Hexa
Page number
Page 0
Page 1
Page 2
Page 3
Page 4
address
60000
60100
60200
60300
60400
604FF
Segment Page | Block
6 00 6 01 6 02 6 03 6 04 | 012 000 019 053 A61
(a) Logical address assignment
(b) Segment-page versus
memory block assignment
Memory Management Hardware

## Slide 34: LOGICAL TO PHYSICAL MEMORY MAPPING
Segment table
0
F
6
35
A3
Page table
00
35
36
37
38
39
012
000
019
053
A61
012
A3
Physical memory
00000
000FF
01200
012FF
Block 0
Block 12
32-bit word
01900
0197E
019FF
Logical address (in hexadecimal)
6 | 02 | 7E
Segment and page table mapping
Segment | Page | Block
6 | 02 | 019
6 | 04 | A61
Associative memory mapping
Memory Organization 33 Memory Management Hardware

## Slide 35
34
Memory Organization
MEMORY PROTECTION
Protection information can be included in the
segment table or segment register of the memory
management hardware
- Format of a typical segment descriptor
The protection field in a segment descriptor specifies
the Access Rights to the particular segment
In a segmented-page organization, each entry in the page table may have its own protection field to describe the Access Rights of each page
- Access Rights:
Full read and write privileges. Read only (write protection) Execute only (program protection) System only (O.S. Protection)
Base address | Length | Protection
Memory Management Hardware